## Slide 1
MTS hybrid multicast — architecture overview
On-premises
Sender
172.20.51.10
CGW · AS 65000
Lo0 172.20.255.1
PIM RP
UDP 239.1.1.1
Direct Connect
Transit VIF ×2
GRE
AWS Cloud
DXGW
AS 65300
Region ap-northeast-2
Transit Gateway
AS 65400
VPC 10.1.1.0/24
AZ1 · ap-northeast-2a
TGW subnet
Router subnet
Receiver subnet
AZ2 · ap-northeast-2c
TGW subnet
Router subnet
Receiver subnet
TGW multicast domain · IGMPv2
TGW attachment
C8000V-1 · active
Gi1 .30 · GRE endpoint
C8000V-1 Gi2
10.1.1.90
EC2-1 receiver
10.1.1.84
TGW attachment
C8000V-2 · standby
Gi1 .40 · prepend ×3
C8000V-2 Gi2
10.1.1.100
EC2-2 receiver
10.1.1.116
GRE
failover
TGW replicates
VPC Route Server
AS 65100
BGP·BFD
BGP·BFD
tgw-rtb · receiver-rtb
→ active C8000V Gi1
route inject
GRE Tunnel100 (overlay) · 172.20.255.1 → anycast Lo0 10.255.255.1 · eBGP 65000↔65200 + PIM
Solid: data path · dashed: failover path and control plane — only the active router sends on Gi2

## Slide 2
GRE-encapsulated packet path (on-prem → AWS)
On-premises
CGW · GRE encap
outer 172.20.255.1 → 10.255.255.1
Direct Connect
Transit VIF ×2
GRE
AWS Cloud
DXGW
Region ap-northeast-2
Transit Gateway
TGW route table
10.255.255.1/32
→ VPC att (static)
VPC 10.1.1.0/24
TGW subnet · AZ1
Router subnet · AZ1
Router subnet · AZ2
TGW attachment ENI
tgw-rtb lookup ← RS
10.255.255.1/32
→ active C8000V Gi1 ENI
C8000V-1 · active
GRE decap
GRE
C8000V-2 · standby
prepend ×3
failover
VPC Route Server
BGP best path → next hop
injects /32
On-prem → AWS GRE packet path — the /32 in tgw-rtb picks the router that receives the tunnel